## Slide 1
Full Scale In-Situ Gaseous Reduction of Hexavalent Chromium in Vadose Zone Soils with H2S Gas
Brian Hitchens, PG, CHG, RG,
Chad Bird, PE, and Kirk Craig, PE

## Slide 2: Introduction
In-Situ Gaseous Reduction for CrVI is a new approach to address a common issue
First applied in 1998 at the White Sands Missile Range as a cooperative DOE/DOD pilot study
The approach has significant benefits including:
  Improved distribution through vadose zone soils as compared to liquid reductants
  Rapid reaction and treatment times
  Reduced potential for mobilizing CrVI to groundwater
Significant drawbacks include safety considerations during implementation

## Slide 3: Introduction
Theory and historical testing of In-Situ Gaseous Reduction concept
Full scale case study implementation
Considerations for future applications

## Slide 4: ISGR Chemistry
The stoichiometric equation for the volume of H2S required to reduce CrVI to CrIII is:
0.375 moles of H2S to reduce 1 mole of CrVI to CrIII
Approximately 4 mg H2S per mg CrVI on a mass/mass basis (perfect reaction with no competing H2S sinks)
Catalytic effects in the soil matrix may greatly accelerate oxidation of H2S:
8CrO42- + 3H2S + 10H+ + 4H2O → 8Cr(OH)3 + 3SO42-
H2S + 2O2 → SO42- + 2H+

## Slide 5: Historical Pilot Study
1998 White Sands Pilot Test:
Targeted a 10’ ROI to 18’ BGS
Sand to silty-sand lithology
200 ppmv injection concentration
35’ x 35’ hypalon cover placed over injection site to reduce vertical migration of gas
Operated for 10 weeks
Treatability study: 4x10-5 lb H2S/lb soil
Pilot scale: 6.6x10-5 lb H2S/lb soil

## Slide 6: Project Case Study

## Slide 7: Site Background
  Aerospace Manufacturing Facility
    10 years of plating operations
  Initial characterization showed cadmium and CrVI impacts in soils beneath plating lines
  Void in spill conveyance trench identified adjacent to external wall of building
  Runoff from exterior roof drain downspout increased depth of impacts in CrVI area
  Depth to Groundwater - ~100 feet
  Lithology: intermixed gravel, cobbles, and silt

## Slide 8: Project Goals
  Fast remediation timeline for sale of property, 1 year for:
    Enrollment in VRP
    Complete characterization
    Work-plan development
    Bench scale testing
    Permitting
    Full scale implementation
    Reporting
    No Further Action determination
  Constraints:
    Building must remain standing
    No deed restrictions (or long-term monitoring)
    Soils should meet residential screening goals

## Slide 9: Extent of Impacts
  Hexavalent Chromium and Cadmium
  Three impacted areas identified
  Northern area: Cadmium impacts to 7 ft bgs
  Southern area:
    Cr6+ impacts to 95 ft bgs (up to 7800 mg/kg)
    Above rSRLs (30 mg/kg) to 45 ft bgs
    No groundwater impacts
  Alternatives Evaluated:
    Excavation
    Immobilization
    In-Situ Reduction
    In-Situ Gaseous Reduction

## Slide 10: Remedial Design
  Shallow Excavation of impacts to 10’
  ISGR of deeper CrVI impact above residential soil screening levels (30 mg/kg)
  All cadmium impacts were within the top 7-feet of soil
  Deep CrVI impacts constrained to a small area near the suspected release point
  ISGR area backfilled with 1-foot of hydrated bentonite prior to backfill

## Slide 11: Injection Design
  ISGR treatment interval from 10-45’ BGS
  Focus on a safe, efficient, uniform distribution of H2S gas in treatment interval
  10-Foot radius of influence
  Injection well with three, nested10-foot well screens
  Extraction wells with single 35-foot well screens

## Slide 12: Well Design
10
20
30
40

## Slide 13: Bench Scale Testing
  Bench scale test:
    Passed H2S gas through
    columns of homogenized soil
    Evaluated H2S concentrations
    and exposure duration
    Calculated mass H2S/mass soil
    treated
    Results
      Recommended concentration of 400 ppm
      Injected at 60 cfm
      For 16 weeks of injection

## Slide 14
200 ppm H2S Bench Study Results

## Slide 15
400 ppm H2S Bench Study Results

## Slide 16: Calculation of H2S Dosing
Observed efficiency was ~3.7x – 5.0x theoretical requirement.
Did not collect data on H2S breakthrough from soil columns, cannot say if the observed efficiency is due to unused H2S passing through column, or oxidation of H2S. We will include this evaluation in future bench-tests.
Calculated volume of H2S for application was based on mass of SOIL in treatment area with assumed average CrVI concentration of 376 mg/kg
  Recommended dosage: 340 mg H2S/Kg soil.
  Goal: Apply 780 kg H2S evenly throughout 340 cubic yards of treatment area
Safely

## Slide 17: How Fast To Apply?
Higher application concentrations and flow rates reduce treatment time, but increase risk:
  Leaks
  Inefficient application (breakthrough of unreacted H2S)
Target rate is 90 CFM injection at 500 ppm H2S, 120 CFM extraction
  Injection time: 9 weeks (continuous)

## Slide 18: ISGR System Construction

## Slide 19: Well Construction
10-20’
22-32’
34-44’
  Triple nested injection well to provide improved vertical control of H2S Distribution
  Extraction wells single screened from 10-45’

## Slide 20: Distribution System

## Slide 21: Delivery System

## Slide 22: Health and Safety
  H2S Monitoring/Alarms
    In gas cabinet (injection stops, extraction continues to maintain negative air flow in cabinet)
    In ambient air (full shutdown)
    In stack (full shutdown)
    Autodialer to Fire Department and 24 hour alarm response team
    Backup battery powered monitoring/alarms
  Placarding
  All cabinet work or alarm response in Level B

## Slide 23: Alarm Situation
  Autodialer callout on a Sunday afternoon
    H2S detected in Cabinet >10 ppm
  Fire department and designated project emergency personnel responded
    Fire Department responders not adequately prepared for H2S, notwithstanding extensive notifications
  Alarm in cabinet, but not ambient
    Diagnosed as a loose rotameter connection

## Slide 24: Alarm Diagnosis
Initial Alarm: H2S drawn into cabinet through louvers
Turning on power to system (gas off, blowers off) caused second ambient air alarm
Due to residual H2S in feed line, released as solenoids opened
After repair, full leak check with Helium

## Slide 25: Results!
1
2
3
4
5
6
Preferential Flow Direction

## Slide 26: Results!
12’ 20’ 32’ 38’
Samples collected after 8 weeks of injection
Field screening of soils from drill cuttings showed generally good reduction, with pockets of remaining CrVI

## Slide 27: Results!
Confirmation results ranged from ND<0.04 mg/kg to 140 mg/kg
95% UCL of post-remediation CrVI concentration:
16.34 mg/kg
98.8% reduction in overall CrVI
South
1,180
537
88.8
60.6
38.2
159
75.0
ND<0.050
0.720
0.516

## Slide 28: ISGR Cost
ISGR treatment of ~410 yards of soil: ~$250,000
  Approximately $650/yard
  Includes:
    Treatment Skid
    Well Installation (7 sonic wells)
    Permitting
    Labor/monitoring
    H2S supply
    Post-Treatment Characterization (2 borings)
  Unit cost would be reduced for larger-scale implementation

## Slide 29: Excavation Cost
Excavation of ~400 yards of shallow soil: ~$230,000
  Includes:
    Limited access excavation
    Confirmation Sampling
    Backfill
    Re-poured slab
    Transport and Disposal (80% RCRA hazardous)

## Slide 30: Summary
ISGR treatment achieved CrVI remediation goals quickly and cost-effectively
Non-detect results achieved for CrVI throughout the majority of the treatment area
Implementation is difficult, requiring close oversight and extensive H&S precautions
Scaled up treatment of larger soil volumes will improve cost effectiveness, but will also pose additional H&S concerns with H2S storage, management, and delivery

## Slide 31: Questions?